## Slide 1: APA 2026 Annual Conference - FMCSA Update
David Rios – Western Region HM Program Manager
Notes: FMCSA Updates
Incidents
MASFOs

## Slide 2: FMCSA General Updates

## Slide 3: FMCSA Personnel Updates
Headquarters Personnel:
HM Division Chief Paul Bomgardner - Retired
HM Division James Simmons - moved to MARAD
Southern Region HMPM Clay Greene retired.
Suzanne Ellis - Retired

## Slide 4: FMCSA Personnel Updates
Field Personnel:
Western Region HM Program Manager – David Rios
Southern Region HM Program Manager - Vacant
Eastern Region HM Program Manager – Vacant
Midwestern Region HM Program Manager – Jessica Stiles
18 HM Specialists

## Slide 5: FMCSA Regulatory Updates
Railroad Grade Crossings: Notice of proposed rulemaking (NPRM) – May 30, 2025
  Current regulation:
    Drivers transporting certain HM are required to stop before crossing a railroad track.
  Proposal:
    Drivers do not need to stop if the railroad grade crossing is equipped with an active warning device that is not in an activated state.
Notes: Currently certain HM vehicles need to stop at all railroad grade crossings regardless of whether they have gates/warning lights. The proposal will allow them to continue with traffic through railroad grade crossings that have gates/lights that are not activated. This will be the same for buses, too.
A Notification of Data Availability followed the NPRM requesting comments on data provided. That comment period ended this past Spring.

## Slide 6: FMCSA Regulatory Updates
Liquid-Burning Flares: Final rule effective
3/23/26
  FMCSA removed the wording “liquid-burning flares” from the emergency equipment requirements, as this term is outdated and no longer used. Fusees remain in the regulations for emergency equipment that can be used when a vehicle is stopped for an emergency (e.g. is broken down).
  Flame-producing emergency signal use is still prohibited for CMVs transporting 1.1, 1.2, 1.3 and other flammable commodities
Notes: Note that I had AI create this picture for me. Asked it to put a hazmat cargo tank broken down on the side of the interstate with fusees behind it. We have seen that AI doesn’t completely understand HM – it is learning but if you do use AI for anything please double check the info you receive, as it will not necessarily be accurate.

## Slide 7: Hazardous Materials Routing
National Hazardous Materials Route Registry
For maps and a list of Highway Routing Designations for individual States go to:
National Hazardous Materials Route Registry by State

## Slide 8: Incidents

## Slide 9: St. Louis, MO
HOWEVER – shipper stated that the description was “misleading” as they had copied it over from an old one. Indicated the load was actually hazardous waste comprised of 1,000 gallons of a 50% nitric acid solution along with 2,000 gallons of water for 3,000 gallons total in the cargo tank.
Shipping paper showed UN3264, Waste Corrosive Liquid, Acidic, Inorganic, N.O.S. (Nitric Acid, Hydrofluoric Acid), 8, PG II.
Notes: This tends to be an issue with hazardous waste. The generator calls it something but in reality it is a mix of a bunch of things. While they test the material for EPA purposes, they sometimes don’t think to test it for DOT classification purposes too and it ends up misclassified.
I’m not sure what the ultimate determination was, but if I remember correctly the valve had some damage and it was possible that this material reacted with the metal of the valve or a previous material inside the tank. It was a lined cargo tank.

## Slide 10: Anhydrous Ammonia – Weatherford, OK
Notes: Cargo tank parked at a hotel to stay overnight – picked up anhydrous in TX, delivered to several locations in OK, was headed back home to TX at the time of the incident. Driver noticed the leak, spoke to his company, checked it out a couple of times, went in and out of the hotel, and finally called for help. By then the leak was massive. It came from the manway in the bottom of the tank.
Roughly 64 people were exposed, 34 required hospitalization, up to 10 were on ventilators, and 14 emergency responders were exposed. Everyone survived.

## Slide 11: Anhydrous Ammonia – Weatherford, OK
Notes: Left pic – how the leak began. Right pic – after it went on for awhile.
Anhydrous ammonia is placarded domestically as a 2.2 non-flammable gas (green placard) and must be marked with the words “inhalation hazard”. It expands at a rate of 850:1, meaning 1 gallon of liquid anhydrous ammonia instantly vaporizes into about 850 gallons of gas. So it expands and spreads very fast.

## Slide 12: Multi-Agency Strike Force Operations (MASFOs)

## Slide 13: Mid-West Service Center MASFO’s
Fireworks
Nurse Tanks

## Slide 14: Section Header (Times New Roman, Bold, 50)
Upcoming:
Fireworks MASFO in Ohio in May
Other fireworks initiatives across the Midwest, focused on inspecting trucks headed to shows and picking up from wholesalers

## Slide 15: Ohio Nurse Tanks
PHMSA, Ohio PUCO, FMCSA
Conducted inspections on 41 different companies
Covered 1,421 nurse tanks
Notes: We physically checked all 1,421 nurse tanks over the span of 4 days. In the cold, then in the heat.

## Slide 16: Ohio Nurse Tanks
A total of 171 probable violations were observed and cited – 12.03%.
Violations included:
  Failure to test
  Marking/labeling
  Not securely connected

## Slide 17: Operation Flash Point
FMCSA’s Western Region conducted a Multi-Agency Strike Force Operation (MASFO) along the Texas southern border.
Participating Agencies:
FMCSA
PHMSA
Texas Dept. of Public Safety
Texas Comptroller of Public Accounts
U.S. Customs & Border Protection
Homeland Security Investigations

## Slide 18: FMCSA TX Border Inspection Facilities
Focus: Illegal transportation of diesel fuel, English Language Proficiency (ELP), HM

## Slide 19: Southern Border MASFO

## Slide 20: Eagle Pass POE

## Slide 21: Ysleta POE

## Slide 22: Cargo Tank Inspections

## Slide 23: Southern Border MASFO
Notes: What do you see regarding the placards?
The video shows diesel fuel leaking from undeclared HM. Explain diesel smuggling issue here. Diesel must be sold in MX from MX producers – it is not allowed to be brought into MX and sold. So they are getting creative by adding fuel tanks to truck-tractors and filling them with diesel fuel then smuggling the fuel into MX. They do not take great care of the tanks, and they aren’t well-made packages, so a surprising number of them were leaking when we inspected them. More to follow on the next slide.

## Slide 24: Truck-Tractor / Multiple Tanks

## Slide 25: Southern Border MASFO
Notes: Anything wrong with this placard? (we did not adopt the NOMs for use in the U.S. – this placard is approved in Mexico but not U.S.)
What about this tube trailer? (Cargo tank test date/markings on a tube trailer, also though not shown the numbers on the placard are possibly too small vertically)

## Slide 26: Operation FP Outcomes
FMCSA Staff
323 Inspections
32% Hazmat OOS Rate
27% Vehicle OOS Rate
4% Driver OOS Rate
37% of Drivers failed English Language Proficiency (ELP) Assessment
35 investigation referrals

## Slide 27: HM Safety Permit
Notes: USC5109 requires a permit for certain materials.

## Slide 28
PHMSA Registration
49 C.F.R. 107.601
Any amount of HM that requires placarding
A quantity of HM in a bulk packaging with a capacity equal to or greater than 3,500 gallons for liquids or gases, or more than 468 cubic feet for solids.
HMSP
49 C.F.R. 385.403
Highway route-controlled quantity of Class 7
More than 55 pounds net weight of Division 1.1, 1.2, or 1.3 material
An amount of Division 1.5 that requires placarding
>1 liter of PIH Zone A
PIH Zone B in a bulk packaging
PIH Zone C or D in a packing with a capacity equal to or greater than 3,500 gallons.
Methane (liquefied or compressed), natural gas (liquefied or compressed), or any other compressed or refrigerated liquefied gas with a methane content of at least 85%, in bulk packaging with capacity equal to or greater than 3,500 gallons.
Security Plan
49 C.F.R. 172.800
Any quantity 1.1, 1.2, 1.3
1.4, 1.5, 1.6 requiring placards
Large bulk quantity 2.1
Large bulk quantity 2.2 subsidiary 5.1
Any quantity PIH
Large bulk quantity 3 PG I or II
Desensitized explosives 4.1 or 3 requiring placards
Large bulk quantity 4.2 PG I or II
4.3 requiring placards
Large bulk quantity of 5.1 PG I or II
Large bulk quantity 5.1 perchlorates, ammonium nitrate, ammonium nitrate fertilizers, ammonium nitrate emulsions, suspensions, or gels
Any quantity organic peroxide type B liquid or solid temperature controlled
Large bulk quantity 6.1 material (poison)
Large bulk quantity 8 PG I
CDC/Dept of Agriculture select agents or toxins
Uranium hexafluoride requiring subsidiary placarding.
Certain other radioactive HM (Class 7).
Notes: Closing slide that brings it all together. These are three completely different documents and all three have different applicability requirements.
PHMSA’s hazmat registration has the least writing but includes the most HM (more carriers are subject to this requirement). A security plan is required for fewer carriers than those who require the HM Registration, and an HMSP is required for even fewer carriers.

## Slide 29: HMSP Definition
49 C.F.R. 385.402
  Safety Permit - a document issued by FMCSA that contains a permit number and confers authority to transport in commerce the hazardous materials listed in §385.403.
49 C.F.R. 385.403
  A motor carrier may not transport in interstate or intrastate commerce any of the following hazardous materials, in the quantity listed for each, unless the motor carrier holds a safety permit:

## Slide 30: Who needs an HMSP? 49 C.F.R. 385.403(a)
Highway route-controlled quantity of Class 7 (radioactive) material
Notes: The placard pictured in the slide includes a square background – this is required for HRCQ placards (172.507).

## Slide 31: Who needs an HMSP? 49 C.F.R. 385.403(b)
More than 55 pounds net weight of Division 1.1, 1.2, or 1.3 explosive materials
Notes: If a question gets asked on the 1.2 placard – compatibility groups are not required on the placards when transported by highway (per 172.504(g) and also per the individual placarding section 172.522).

## Slide 32: Who needs an HMSP? 49 C.F.R. 385.403(b)
A quantity of Division 1.5 explosive materials requiring placards
> 1,000 pounds

## Slide 33: Who needs an HMSP? 49 C.F.R. 385.403(c)
More than 1 liter (1.08 quarts) per package of a Material Poisonous by Inhalation (PIH) in Hazard Zone A
Notes: First picture shows Arsine, and special provision 1 in column 7. Special provision 1 means PIH (Poison inhalation hazard) Zone A material.
The picture of the soda bottle is a one-liter bottle. So more than this amount would need an HMSP.

## Slide 34: Who needs an HMSP? 49 C.F.R. 385.403(d)
A bulk packaging containing a Hazard Zone B PIH Material

## Slide 35: Who needs an HMSP? 49 C.F.R. 385.403(e)
A packaging with a capacity equal to or over 3,500 gallons containing a Hazard Zone C or Hazard Zone D PIH Material
Notes: See FMCSA’s Safety Advisory Notice on this issue if necessary. Since NH3 is not assigned to Hazard Zone C or D domestically in the 172.101 table it will not be required to possess an HMSP.

## Slide 36: Who needs an HMSP? 49 C.F.R. 385.403(f)
Compressed or refrigerated liquefied methane OR
Compressed or refrigerated liquefied natural gas OR
Any other compressed or refrigerated liquefied gas with methane content of at least 85%
In a bulk packaging with capacity equal to or over 3,500 gallons.
Notes: The first two listed on the slide fall under UN1971 (Methane, compressed or Natural gas, compressed) and UN1972 (Methane, refrigerated liquid (cryogenic liquid) or Natural gas, refrigerated liquid (cryogenic liquid)).

## Slide 37: Additional Operational Requirements 49 C.F.R. 385.415
Copy of the permit or the permit number must be in the vehicle
Written route plan is required (in the vehicle) for the transportation of:
  Highway route-controlled Class 7 (radioactive) materials (in accordance with §397.101) or
  Division 1.1, 1.2, and/or 1.3 (explosive) materials (in accordance with §397.67)
Must have in the vehicle a telephone number of a carrier representative who can confirm that the shipment is within the planned route
Notes: There is no regulatory requirement to maintain a copy of the HMSP at the carrier’s PPOB. The investigator should confirm the HMSP information in the carrier’s profile or through MCMIS during the investigation.
Written route plan is only required during transportation. THERE IS NO REQUIREMENT TO MAINTAIN THE ROUTE PLAN AFTER THE TRIP HAS BEEN COMPLETETED (no recordkeeping requirement once transportation ends). You can look for a route plan during the investigation but no violation exists if the carrier failed to keep a copy.
Part 397 is where the specific routing requirements are explained for these materials. Specifically 397.67 states that a motor carrier transporting hazardous materials requiring placarding shall operate the vehicle over routes which do not go through or near heavily populated areas, places where crowds are assembled, tunnels, narrow streets, or alleys, except when there is no practicable alternative or an emergency condition exists. States may also designate specific routes where certain HM is not authorized to be transported.
FMCSA provides an HM Route Registry here: https://cms8.fmcsa.dot.gov/regulations/hazardous-materials/national-hazardous-materials-route-registry . There are a few questions about HM routing in the SCR. This is the website you will go to in order to determine if the HM was transported on appropriate routes.

## Slide 38: Additional Operational Requirements – Communications 49 C.F.R. 385.415(c)(1)
A driver transporting any HM that requires an HMSP must make contact with the carrier by telephone, radio, or via electronic tracking or monitoring system at:
  The beginning and end of each duty tour
  The pickup and delivery of each permitted load
The carrier must maintain a record of communications for 6 months after acceptance of the shipment for which an HMSP is required. The record must contain:
  Name of driver
  ID of vehicle
  Permitted material(s) being transported
  Date, location, time of each required contact
Notes: “Electronic tracking or monitoring system” includes ELDs. If ELDs are used for communication, the carrier must still maintain a communication record that contains all required information, if the ELD does not contain all required information.
This includes private carriers.
*** eFOTM 8.1.6 – Owner operators are exempt from this requirement.
Owner/operators transporting under their own authority, or if the only phone number for the motor carrier is the driver’s cell phone number, are not required to maintain a communications plan or log.

## Slide 39: FMCSA Enhanced Oversight HMSP – What to Expect
Onsite
Comprehensive
  Federal Motor Carrier Safety Regulations
  PHMSA HM Regulations
Notes: Investigative Procedures -- Enhanced Oversight HMSP Motor Carriers
On a monthly basis, we look at the list of HMSP enhanced oversight carriers and assign those carriers to be investigated by Safety Investigators.
First, it will be onsite. We do this for several reasons. A few are so that we can review your security plan. This is obviously a sensitive security document. We don’t want it transmitted or copied unnecessarily. If we absolutely must obtain part or all of it, significant safeguards are taken. Next, to get a full picture of the operation, the products themselves, how they are stored, the vehicles that transport them, and talking in person, like we are today, is always better for us to get a complete understanding of the safety posture overall.
Second, it will be a comprehensive investigation that will result in a safety rating. The onsite comprehensive investigations must take place within 6 months of the carrier appearing on the list.
Follow the normal procedures for conducting a HMSP investigation.
If at any time before the investigation the carrier no longer meets any of the enhanced oversight conditions, then the carrier may be removed from the enhanced oversight list at the DA’s discretion and the investigation cancelled.
After an enhanced oversight HMSP carrier is investigated and receives a final satisfactory rating that carrier will not be placed on the enhanced oversight list for 24 months.
The Enhanced Oversight conditions are any of these 3 conditions:
The motor carrier has the HM Compliance Basic equal to or greater than the HM threshold for the past 2 consecutive months;
AND/OR
The motor carrier has any 2 or more BASICs, other than the HM Compliance Basic, equal to or greater than their HM thresholds for the past 2 consecutive months (the carrier may have any 2 of unsafe driving, HOS compliance, crash indicator, driver fitness, controlled substances and alcohol, or vehicle maintenance);
OR
The motor carrier has insufficient data which is defined as not enough data to calculate a percentile in SMS during any month of the current 48-month period and in addition to this, the carrier has a safety rating over 4years old.

## Slide 40: What Records to Have Ready
Authority and General Safety Records
  PHMSA HM Registration
  HMSP records (MCS-150B)
  Accident Register
  Fleet Mileage & Operational Data
  CMV and Driver Lists
Proof of Insurance (MCS-90s)
Driver Qualification Documents
  MVRs
  CDLs
  Driver Safety Performance History (DACH, previous employment history, etc.)

## Slide 41: What Records to Have Ready
Controlled Substances & Alcohol Testing Program Records
  Policy
  Testing Consortium/Program Enrollment
  Pre-Employment Test Records
  Random Test Records
  Test Results and Custody Documents
  Additional Testing (Post-Accident, Follow-up, etc)
  FMCSA Drug & Alcohol Clearinghouse Records

## Slide 42: What Records to Have Ready
Hours of Service and Supporting Documents
  Records of Duty Status (Usually ELDs)
  Supporting Documents (tolls, fuel/expense receipts, dispatch records, etc.)
  For ELDs unassigned driving records
Vehicle, Inspection, Repair & Maintenance Records
  Watch for length of leases (30 days or more)

## Slide 43: What Records to Have Ready
Driving, Parking, and Routing Rules (397)
  Copy of part 397 for drivers
  Emergency Contact Procedures & Routing Info
  Signed Receipt
Security Plan
HM Employee Training Records
Communication Plan
Shipping Papers
Emergency Response Information
HM Incident Reports (if applicable)

## Slide 44: Security Plans 49 C.F.R. 172.800 – 172.804

## Slide 45: HM subject to security plan requirements - EXPLOSIVES
Any quantity of a Division 1.1, 1.2, or 1.3 material.
Notes: These are high explosives, such as black powder, bombs, boosters, explosives for blasting, detonating cord, and display fireworks.

## Slide 46: HM subject to security plan requirements - EXPLOSIVES
A quantity of Division 1.4, 1.5, or 1.6 material requiring placarding.
Notes: Remember a quantity that requires placarding is equal to or greater than 1,001 pounds of any combination of table 2 materials. Placards could be required for just the 1.5 materials or for a combination of 1.4, 1.5, and 1.6 materials.
1.4 is used for some detonators and detonating cord and is also used for consumer fireworks.
1.5 is most commonly seen by FMCSA with ammonium nitrate fuel oil mixture (ANFO), seen in the picture on the right side of this slide, and transported by and to blasting companies.
1.6 is not seen as frequently, but it will occasionally be transported in commerce.

## Slide 47: Components of a Security Plan and Record Retention Requirements

## Slide 48: Components of a Security Plan Assessment
The carrier must assess their specific transportation security risks
The assessment must include site specific risks for facilities where any of the HM listed on the previous slides is prepared for transportation, stored, or unloaded incidental to movement.
Notes: Here’s a link to PHMSA’s security plan guidance brochure. https://www.phmsa.dot.gov/sites/phmsa.dot.gov/files/docs/Enhanced%20Security%20Brochure.pdf
The carrier must assess their own risks - we do not tell them what the risks are.

## Slide 49: Components of a Security Plan
The security plan must include appropriate measures to address the assessed risks. At a minimum, the plan must include these elements:
  Personnel Security
  Unauthorized Access
  En Route Security
Notes: FMCSA does not require the carrier follow any specific measures, just that they assess their own risks and follow the appropriate measures to alleviate those risks within each element listed on the slide.
Personnel Security includes measures to confirm information provided by job applicants for employees who will handle the HM listed on the previous slides.
Unauthorized Access includes measures to address the assessed risk that unauthorized people may gain access to the HM listed on the previous slides or to the transport conveyances that will be used to transport the HM.
En Route Security includes measures to address the assessed risks from origin to destination, including shipments stored incidental to movement.

## Slide 50: Components of a Security Plan Additional Information
The security plan must also include:
  Identification by job title of the senior management official responsible for overall development and implementation of the plan; and
  Security duties for each position or department that is responsible for implementing the plan or a portion of the plan, and the process of notifying employees when specific elements of the security plan must be implemented; and
  A plan for training HM employees in accordance with 49 C.F.R. 172.704(a)(4) and (a)(5) (Security Awareness Training and In-Depth Security Training).

## Slide 51: Security Plan Record Retention Requirements
The plan must be in writing.
It must be retained for as long as it remains in effect.
The plan must be reviewed at least annually and revised and/or updated as necessary to reflect changing circumstances (i.e. facility moved, transporting new product, etc.).
The most recent version of the plan must be available to the employees who handle the HM covered by the security plan and to those who are responsible for implementing it.
The plan (or an electronic file thereof) must be accessible at or through the carrier’s PPOB.
Notes: There is no requirement to retain previous versions of the security plan – only the current version must be retained. If you feel that the carrier created the plan the night before you arrived for the investigation, ask them to see the word or pdf document on the computer. Have them right click and show you the properties and you can see when the document was created.
There is no requirement for the carrier to retain written evidence that they reviewed the plan annually. You will need to interview the relevant company officials to determine if a violation exists.
Much like with shipping papers, any document that meets all of the applicable criteria can be called a security plan. Even if the document was written to meet another agency’s security plan requirements (172.804).

## Slide 52: Security Plans – Sensitive Security Information Markings
If FMCSA does retain a copy of a security plan, a special header and footer must be included on the document (if not already there).
Header:
SENSITIVE SECURITY INFORMATION
Footer:
WARNING: This record contains Sensitive Security Information that is controlled under 49 CFR parts 15 and 1520. No part of this record may be disclosed to persons without a “need to know”, as defined in 49 CFR parts 15 and 1520, except with the written permission of the Administrator of the Transportation Security Administration or the Secretary of Transportation. Unauthorized release may result in civil penalty or other action. For U.S. Government agencies, public disclosure is governed by 5 U.S.C. 552 and 49 CFR parts 15 and 1520.
Notes: Do not copy a security plan – eFOTM 8.1.3.5 near the bottom in the security plans section. Policy – Interim Policy on the Handling, Safeguarding, and Accessibility of Security Plans MC-ECH-004-06.

## Slide 53: Security Plan
Are you following your plan?
Notes: If the carrier’s plan says that they are going to follow specific security measures, then they must follow those measures or they are in violation of the regulations (failing to adhere to their security plan).
Many carriers get security plan templates from Google, and these plans are often outdated or do not match the carrier’s specific operations. Examples of measures included in security plans:
The storage facility will have motion activated lights installed and a chain link fence around the perimeter. Go to the site and check for motion activated lights and a chain link fence.
Fencing will be inspected at a specific interval and inspection reports will be written, then retained on file. Check for fence inspection reports.
Trucks will be locked with a padlock when transporting HM that is covered by the plan. Check for padlocks and keys.
Drivers will be provided with cell phones. Are they?
Visitors must sign in upon entrance to the facility. Look for a sign in sheet.

## Slide 54: Common Security Plan Violations
49 C.F.R. 172.800(b) – Acute – Offering for transportation or transporting one or more hazardous materials listed without developing and adhering to a security plan that conforms to the requirements of 49 CFR Subpart I.
49 C.F.R. 172.800(b) – Acute – Offering for transportation or transporting a hazardous material listed without a security plan.
49 C.F.R. 172.800(b) – Acute – Failing to adhere to a required security plan.
Notes: These are the only acute security plan violations. There are no critical security plan violations. Note that every violation shown on this slide uses the same section number – you must pick the most appropriate of these three options when citing this violation.

## Slide 55: Common Security Plan Violations
49 C.F.R. 172.802(a) – Failing to include an assessment of possible transportation security risks for shipments of hazardous materials listed in section 172.800 as part of the security plan.
49 C.F.R. 172.802(a)(1) – Security plan fails to provide measures to address Personnel Security.
49 C.F.R. 172.802(a)(2) – Security plan fails to provide measures to address Unauthorized Access.
49 C.F.R. 172.802(a)(3) – Security plan fails to provide measures to address En Route Security.

## Slide 56: Common Security Plan Violations
49 C.F.R. 172.802(b) – Security plan fails to include all required information.
49 C.F.R. 172.802(c) – Failing to revise and/or update the security plan at least annually or due to changing circumstances.
49 C.F.R. 172.802(c) – Failure to make copies of security plan available to hazmat employees.
49 C.F.R. 172.802(c) – Failing to notify all employees responsible for implementing a security plan of any updates or revisions.
49 C.F.R. 172.802(c) – Failure to conform all copies of the security plan to the latest revisions.
49 C.F.R. 172.802(d) – Failing to maintain a copy of the security plan at the PPOB or make it available upon request.

## Slide 57: Security Sensitive Information
A security plan is “sensitive security information” (SSI)
  49 CFR 1520.13
    Protective Marking (Header)
    “Sensitive Security Information
    Distribution Limitation Statement (Footer):
    “WARNING: This record contains Sensitive Security Information that is controlled under 49 CFR parts 15 and 1520. No part of this record may be disclosed to persons without a “need to know”, as defined in 49 CFR parts 15 and 1520, except with the written permission of the Administrator of the Transportation Security Administration or the Secretary of Transportation. Unauthorized release may result in civil penalty or other action. For U.S. government agencies, public disclosure is governed by 5 U.S.C. 552 and 49 CFR parts 15 and 1520.”
Notes: We only copy the security plan when necessary to demonstrate that the motor carrier failed to comply with the applicable security plan regulations.
Ask the carrier to mark the plan first and if they refuse to do so, make sure to mark it yourself and explain that you marked it in your AIM comments. These markings help to prevent accidental release during FOIA requests or at any other time. Required

## Slide 58: Contacts
Jessica Stiles
Hazmat Division Chief (acting)
FMCSA
U.S. Department of Transportation
(360) 846-3869
Jessica.Stiles@dot.gov
David Rios
HM Program Manager
Western Region
FMCSA
U.S. Department of Transportation
(503) 949-6250
david.rios@dot.gov